### HWg-STE  Ethernet thermometer

Web thermometer with a LAN connection and free software for creating MS Excel reports

The HWg-STE is a web thermometer with built-in web interface and SNMP support. Sends an e-mail alert if the temperature goes out of a specified range. Supports SNMP.

Free Windows logging software HWg-PDMS included. Graph data overview and MS Excel export

  - Supplied with an AC power adapter and a temperature probe

  - Simple installation, supports DHCP

  - A second probe (temperature or humidity) can be connected

  - Free Windows software for displaying graphs

  - Easily create a graph of temperature in MS Excel

Typical applications include monitoring the temperature of equipment, computers or disk arrays, or monitoring HVAC operation.

Online demo: http://hwg-ste.hwg.cz

- Ethernet: RJ45 (100BASE-T)

- WEB: Built-in Web server

- Sensors: 1xRJ11 1-Wire (max 2 temperature / humidity probes)

- M2M communication protocols: SNMP, XML

- Alerts (value out of defined safe range):  E-mail

- HWg-PDMS software: Logging of values, graphs, export to MS Excel

# Text boxes

Keywords:

temperature monitor, ethernet thermometer, ip thermometer with email alerts

web thermometer, SNMP thermometer, snmp, excel reports, email alerting, Ethernet temperature, temperature report, humidity report