### IP WatchDog HWg-WR02a: ping restarter, web watchdog

Monitors two devices over IP (PING/WEB) or serial line (RS-232), automatically restarts any of them if it stops responding – autonomous ping relay restarter.

The IP WatchDog WR02a periodically monitors the functionality of a device by transmitting or receiving a defined  “I'm alive and OK” signal. This signal can be received over IP (PING or WEB) or RS-232 (serial port). If the correct reply is not received in time, the controlled device is restarted using a relay.

The IP WatchDog is a ping relay for 230V or simply ping restarter with two relay outputs. It can monitor two devices (two independent channels, two relays).

Each channel can be used for autonomous restart or switched on/off as web relay.

The IP WatchDog WR02a allows flexible configuration – method of functionality detection, switchoff time when restarting.

Industrial applications can benefit from DIN rail mount and internal relays that can directly switch 110/230VAC, max 16A. Failures are detected with five distinct methods, separately for each channel (Ping Tx/Rx, Web page Tx/Rx, RS-232 Rx data).

- Online demo: http://ipwatchdog.hwg.cz

- Ethernet: RJ45 (10BASE-T)

- WEB: Built-in web server, manual reset and output control, logging

Functions: 2 channels, independent monitoring of two devices

- Methods of detecting functionality:

  - Ping Push: IP WatchDog periodically sends PING requests

  - Ping Request: IP WatchDog waits for a PING request from a specified IP address

  - WEB Push: IP WatchDog periodically requests a web page from a specified address (error 404 detection)

  - WEB Request: IP WatchDog waits for a request for its internal WEB page

  - RS232 Rx: IP WatchDog waits for a sequence of characters in the RS-232 data stream

- Output channel: Relay output (110/230VAC / 16A)

# Text boxes

Keywords:

ping relay 230V, ping power, remote reboot, ping restarter, web watchdog

Web relay 110V, IP address restart, network watchdog, ping automatically reboot, ping boot, IP address monitoring, autonomous restart, ping heartbeat