### HWg-SH2: Cabinet IP access system for two swing handles

Online cabinet access control system. Controls two swing handles over the Web.

The HWg-SH2 is a networked access control system that controls the front and rear doors of a cabinet. It can work independently with an autonomous lock, or over the Ethernet with the HWg-DCD software.

Configuration and opening of doors over the Web

A door contact for detecting the state of the door (open/closed) can be connected

Digital input: An external lock (RFID or iButton lock) can be connected

Detects entry with a key / forced entry

Standalone operation – Door can be opened with: Key, local lock, WEB interface

With HWg-DCD – Door can be opened with: SMS access code, HWg-DCD admin interface, LAN RFID terminal (e.g. located near the entrance to the room)

The HWg-SH2 is typically used to control access to a rack in a data center. It is usually installed in hosting racks (collocation centers) or restricted-access racks.

HWg-SH2 is a cost-effective solution that is easy to install.

- Ethernet: RJ45 (10/100 Mbit)

- Protocols: SNMP, Syslog, SMTP

- WEB: Built-in Web server

- Electronic Swing Handles: Two HWg-SH1 (Southco H3-EM - Electronic Locking Swinghandle) supported.

- Inputs: 2 digital inputs for door contacts (front/back door)

- Local lock: Digital (dry contact) input for an autonomous lock

- Physical features: Rack mount (on the side), dimensions: 96 x 78 x 30 [mm]

- LAN interface: Secure communication with the HWg-DCD application running on a central server

- Compatible software: HWg-DCD for access control (remote control of rack doors) for data centers

# Text boxes

Keywords SH2:

HWg-SH2, IP Lock control, southco H3-EM, electronic locking, swinghandle lock, rack access system, SNMP

industrial door access system, electric door lock, security access systems, cabinet doors control, access security, cabinet swing handle, lock acs, web control, syslog, email, DIRAK E-LINE, DIRAK basic, dirak swing handle, emka lockagent