### PortBox2: Full RS-232 serial port to Ethernet

PortBox2 connects a RS-232 serial port to the Ethernet. The remote serial port can be accessed on a PC as a VSP (Virtual Serial Port). PortBox2 is unique in that it supports a full serial port (9 pins).

A RS-232/485 to Ethernet converter (also called “terminal server” or “device server”) connects any device with a serial port to the Ethernet.

The full RS-232 serial port simplifies connection of any RS-232 device.

PortBox2 contains a truly full RS-232 serial port (9 pins). The free HW VSP (Virtual Serial Port) driver supports the full serial port. Therefore, PortBox2 is capable of connecting devices that do not work with simplified RS232/LAN converters. 
HW group offers a free “HW VSP Multiport” application that supports up to 100 remote serial ports on a single PC. It can be used for Windows server applications as well (works as a NT service).

PortBox2 unique features include a highly configurable settings (baudrate, data bits, parity, stop bits), full serial port and virtual parity support (9-bit communication).

Application examples include connecting a PLC, a virtual serial printer or a barcode reader to a virtual COM17 on a Windows server.

- Ethernet: RJ45 (100BASE-T / 100 Mbps)

- Configuration: Web, Telnet

- RS-232 serial interface: 1x full serial port (9 pins: RxD, TxD, GND, CTS, RTS, DSR, DTR, RI, CD)

- RS-485 serial interface: Yes, up to 115,200 Bd

- Virtual Serial Port: HW VSP free of charge for Windows (NT service, incl. x64 systems). Supports up to 100 remote serial ports.

- Special functions: 9th bit support for RS-232/485 protocols

- Box-2-Box mode: Two PortBox units can be connected back-to-back over the network

- M2M protocols: http, UDP, Telnet, TCP Server, TCP Client/Server

- Support for programmers: HWg-SDK

- Advantages: Native support in the “HW VSP” application – the world's most popular virtual serial port for Windows.

# Text boxes

RS-232 devices

- Barcode reader

- RFID reader

- Serial printer

- LCD display

- Modem interface

- Access control system

- PLC devices

Klíčová slova:

PortBox2, sériový port na Ethetnet, plný sériový port, com na Ethernet, plný sériový port, device server, konvertor sériového portu, virtual serial port pro windows, podpora devátého bitu, serial terminal server

com port na ethernet, ethernet com port, plný sériový port na IP, Device server, virtual serial port zdarma, terminal server, plný rs-232 přes LAN, RS-232/485 na IP,

Keywords:

PortBox2, serial port to Ethernet, full serial port, com to ethernet, full rs-232 device server, serial converter, virtual serial port for windows, 9th bit support, serial terminal server

com port to ethernet, ethernet com port, full serial port to IP, Device server, free virtual serial port, terminal server, full rs-232 over LAN, RS-232/485 to IP