### Poseidon 3468: IP Thermostat with 230V relays

Web enabled thermostat with temperature/humidity measurement, four dry contact inputs and two 110/230V relay outputs. Industrial version, supports SNMP and E-mail, DIN rail mount.

The Poseidon 3468 is designed for industrial alerting applications. Based on the sensor values, the Poseidon 3468 sends alerts and activates outputs.

Relay outputs can directly switch 110/230VAC. The product is fully CE / FCC compliant.

Each value out of the safe range can trigger an alert by e-mail or SNMP trap. Different safe range can be defined for temperature, humidity or dry contact inputs.

When an input contact is closed, the Poseidon sends an e-mail or a SNMP trap. The alert can be delayed by a defined time. (e.g. an e-mail is sent if a cabinet door has been open for more than 5 minutes).

Both relay outputs can be controlled remotely over the Web, or from a software application (XML, SNMP).

A typical application is an “IP thermostat” or an “IP hygrostat”. The relays control heating or cooling (fan) using a temperature or humidity probe. The IP relay 110/230V can be controlled remotely over the Web.

- Online demo: http://poseidon-3268.hwg.cz/values.xml

- Ethernet: RJ45 (10BASE-T)

- Web: Built-in web server

- Sensors: 2xRJ11 1-Wire (max 4 temperature/humidity probes)

- Digital Inputs: 4 digital inputs (dry contact)
(door contact, smoke detector, 110/230VAC supply detector, water leak detector, cooling fan failure detector)

- Digital Outputs: 2 relays (230VAC/16A)
(air conditioning, server power, horn/light tower)

- Local built-in functions: Control of output using a digital input value or a probe value (“thermostat” / “hygrostat” mode)

- Alerts (value out of defined safe range): SNMP trap, E-mail

- M2M communication protocols: SNMP, XML

- Support for programmers: HWg SDK

- Supported software

  - HWg-PD Trigger: Alert redirection to SMS, pop-up messages, PC shutdown...

  - HWg-PDMS: Logging of values, graphs, export to MS Excel

  - CapTemp: Visualization on a map, control of outputs, alarm redirection to SMS

  - Third-party SNMP software

# Text boxes

Keywords:

IP thermostat, web enabled thermostat, IP relay 110V, web relay 230V

modbus relay, snmp relay, digital thermostat, humidity controller, ip relay, hygrometer, two thermostats