### Damocles 1208: I/O over Ethernet

Ethernet relay with 12 digital inputs, 8 outputs, and a Web interface. Industrial model, DIN rail mount. M2M support (SNMP, XML, Modbus/TCP).

The Damocles 1208 provides digital inputs (DI) and digital outputs (DO) that can be remotely controlled over the Web.

Inputs and outputs can also be controlled using M2M protocols over IP (SNMP, Modbus/TCP, XML over HTTP).

When an input contact is closed / opened / changed, the Damocles sends an email with configured text and/or a SNMP Trap.

In a typical application, the Damocles 1208 is used to connect I/O over the Ethernet.  Digital outputs match the digital inputs of another unit (Box-2-Box mode).

Box-2-Box mode:

Press a button in London to turn on a light in Los Angeles. No software is needed. The event of closing a contact at the input of one unit (A) is transferred over the network (SNMP Trap) and switches an output of another unit (B). The Damocles 1208 can react to changes at the inputs of another Poseidon or Damocles unit (without any additional software).

Example: 	High temperature at the air conditioning outlet (Poseidon 3262) turns on a warning light in the IT department in another building (Damocles output).

- Online demo: http://damocles-2404.hwg.cz/values.xml

- Ethernet: RJ45 (10BASE-T)

- Web: Built-in web server, GUI for configuration

- Digital Inputs: 12 digital inputs (for dry contacts)

- Digital Outputs: 8 outputs (open collector, 24VDC)

- M2M communication protocols: SNMP, XML, Modbus/TCP

- Reaction to changes at the input: SNMP trap, Email (editable text)

- Box-2-Box mode: Outputs are activated by alerts from other devices (Poseidon / Damocles)

- HWg-PD Trigger: Alert redirection to SMS, pop-up messages, PC shutdown...

- HWg PDMS: Logging of values, graphs, export to MS Excel

- CapTemp software: Visualization on a map, control of outputs, alarm redirection to SMS

# Text boxes

Keywords:

remote output control, I/O over Ethernet, I/O snmp, I/O xml, dry contact snmp,

dry contact xml, DO control remote, web I/O, modbus/tcp I/O, SCADA I/O, M2M IP I/O, dry contact email